# L I V A  |  multidirectional baffle louvre – mounted on substructure [U 94]

Multidirectional blade baffle louvre – type L I V A, consisting of a substructure [U-shaped carrier as primary profile] and baffle carrier as secondary profile.

Blade baffle louvre L I V A - consisting of a secondary carrier with mounted sheet baffles which are arranged at right angles to each other.

The specially perforated U-94 carrier [primary profile] is suspended rigidly from the mounting level [e.g. bare ceiling] by means of M6 threaded rods using technical approved dowels [distance of the suspensions according to EN 13964].

The distance between the U-shaped carriers depends on the specified module dimension – according to the length of the secondary profile.

The blade baffles of the blade baffle louvre type L I V A are non-perforated and arranged at right angles to each other.

The blade baffles are mounted at the module spacing and consist of baffles of various height / width.

The secondary profiles are perforated for connecting the panels and the U94 -carriers by means of retaining springs [C 94 clips]. The individual secondary profiles are self-adjusting and can be individually hinged open. A non-interchangeable marking [punched holes] ensures the correct alignment of the secondary profiles.

Typically, the edge connection is carried out by means of a shadow gap.

All parts are made of pre-coated aluminium.

Observe the installation manual.

Multidirectional baffle louvre, durlum product – type L I V A or equivalent consisting of:

| Pos. m² | Delivery and installation of panel elements - Multidirectional baffle louvre – type LIVA Secondary profile length: ( 1200 mm Material thickness: approx. 0.6 - 0.8 mm Baffle size: Height: ( 100 mm ( 150 mm ( 200 mm Width: ( 74 mm ( 98 mm Colour: ( standard white [other colours on request] Material: Aluminium - pre-coated on both sides |
| --- | --- |
| Pos. m² | Delivery and installation of a substructure for baffle louvre – type LIVA U-profile - U94 carrier [distance between carriers corresponds to the length of the secondary profile] Colour: optionally ( standard white or  standard black Length: 2400 mm U-profile connector (V94) Colour: optionally ( standard white or  standard black Retaining springs (C94 clips) 2 pcs/secondary carrier Unit price … €/m² Total price … € |